RTCD13N  SERIES    (Warranty of 1,000,000 cycles at 40℃)

●Compliant to the RoHS directive.

●High-reliability series charge/discharge for welding machine.

●Guarantees charge/discharge warranty of 1,000,000 cycles at 40℃

(Useful of 3,000,000 cycles at 40℃)

■Product Specifications

| (unit: mm) | Items | Specifications |
| --- | --- | --- |
|  | Temperature range | -25℃～+70℃ |
|  | Rated voltage | 200～475V.DC |
|  | Capacitance tolerance | ±20% (20℃, 120Hz) |
|  | Leakage current | 0.01CV (μA) or 5 mA,whichever is smaller or less |
|  |  | [ C=nominal capacitance (μF),V= rated voltage (V) ] |
|  | Dissipation factor | Less than the value specified in the standard products table. |
|  | Durability | The rated voltage is applied 1,000,000 cycles a period of one second temperature of 40℃. Following specifications shall meet after the test: (0.8second charge and about 1m second discharge time constant) at a temperature of 40℃. Following specifications shall meet after the test: Capacitance tolerance : ±20% or less of the initial value Dissipation factor : 200% or less of the specified initial value Leakage current : 200% or less of the specified initial value |
| ΦD | P | S | T | Cap material |  |  |  |
| 36 | 12.7 | M5×10 | 6.0 | Phenol |  |  |  |
| 51 | 22.0 | M5×10 | 5.5 | Phenol |  |  |  |
| 64 | 28.6 | M5×10 | 5.5 | Phenol |  |  |  |
| 77 | 32.0 | M5×10 | 4.5 | Phenol |  | standard | JIS C 5101-4 |

|  |  | Part number(Example): RTCD13N 475V 1,000μF±20% E case（Φ77mm）product |
| --- | --- | --- |
|  |  |  |  |  |  |  | RTCD13N 2X 102 Y E 155 M D 5 Series Voltage Code Capacitance code Mounting style Diameter code Length Cap. tolerance Diameter Terminal Type of screw |

■Standard Products Table

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Part number |
| --- | --- | --- | --- | --- |
| 200(2D) | 33000 | 90×160 | 0.15 | RTCD13N2D333YF160M |
|  | 36000 | 90×160 | 0.15 | RTCD13N2D363YF160M |
| 250(2E) | 22000 | 90×160 | 0.12 | RTCD13N2E223YF160M |
|  | 33000 | 90×196 | 0.12 | RTCD13N2E333YF196M |
| 350(2V) | 150 | 36×100 | 0.05 | RTCD13N2V151IA100M |
|  | 330 | 51×100 | 0.05 | RTCD13N2V331YC100M |
| 450(2W) | 330 | 51×100 | 0.05 | RTCD13N2W331YC100M |
|  | 470 | 51×100 | 0.05 | RTCD13N2W471YC100M |
|  | 1000 | 64×120 | 0.05 | RTCD13N2W102YD120M |
| 475V(2X) | 100 | 36×100 | 0.05 | RTCD13N2X101IA100M |
|  | 225 | 51×110 | 0.05 | RTCD13N2X22WYC110M |
|  | 1000 | 77×155 | 0.05 | RTCD13N2X102YE155M |